## Slide 1: Soil water flow and Darcy’s Law

## Slide 2: Laminar flow in a tube
Poiseuille’s Law, ~1840:
where:
Q = volume of flow per unit time (m3 s-1)
r = radius of the cylindrical tube (m)
p = pressure drop across the tube (Pa)
L = length of the tube (m)
 = viscosity (Pas)

## Slide 3: Macroscopic flow-velocity vector
  the overall average of the microscopic velocities over the total volume considered
  the volume considered must be large relative to the scale of heterogeneity
  the ratio of the path length through the soil pores to the net travel distance is the tortuosity

## Slide 4
insert fig

## Slide 5: Water flux
  the volume of water flowing through a unit cross-sectional area per unit time (V/At)
  units of m s-1 , cm h-1, etc…

## Slide 6: Hydraulic gradient
  the drop in water potential per unit distance in the direction of flow (H/L)
  a driving force for water flow
  units depend on how water potential is specified
    commonly water potential is in units of “head” (e.g. cm of water) and the hydraulic gradient is unitless

## Slide 7: Darcy’s Law
  Henry Darcy; Dijon, France; 1856
  the flux is proportional to the hydraulic gradient
  q = flux
  H/L = hydraulic gradient
  K = hydraulic conductivity; a measure of the soil’s ability to transmit liquid water

## Slide 8
Hpi = 100 cm; Hpo = 60 cm; L = 50 cm; K = 10 cm h-1
q = ?

## Slide 9
H1= 10 cm; L = 50 cm; K = 10 cm h-1
q = ?

## Slide 10: Reading assignment
p. 137-146

## Slide 11
insert Fig. 7.7

## Slide 12: Hydraulic resistance
  the resistance of a specified thickness of a particular soil to water flow (Rh)
  Rh = L/K
  For flow through two soil layers, Darcy’s Law is

## Slide 14: Pore water velocity
  the average velocity of water flow through the soil pores
  water flow takes place through the liquid phase in the pores, not through the whole soil
  pore water velocity > water flux

## Slide 15: Factors affecting hydraulic conductivity
  soil texture

## Slide 17: Factors affecting hydraulic conductivity
  soil texture
  soil water content and matric potential

## Slide 19: Factors affecting hydraulic conductivity
  soil texture
  soil water content and matric potential
  soil structure
  electrical conductivity of the soil solution
  species of cations present
  entrapped air

## Slide 21: Factors affecting hydraulic conductivity
  soil texture
  soil water content and matric potential
  soil structure
  electrical conductivity of the soil solution
  species of cations present
  entrapped air
  viscosity of the soil solution
  soil temperature

## Slide 22: Reading assignment
Infiltration, p.259-265