## Slide 1: Soil water retention curve

## Slide 2: Soil water retention curve
  The relationship between soil matric potential and soil water content
    “matric suction” = - soil matric potential
    Usually soil volumetric water content is used
    Usually determined based on empirical data
  Sometimes called by other names
    Soil moisture characteristic curve
    Soil moisture release curve
    Etc...
  When m = 0, the soil is saturated

## Slide 3
Insert 6.8

## Slide 4: Air-entry suction, e
  the critical value at which the largest surface pore begins to empty
  Coarse textured or well-aggregated soils
    Small e
    Sharp changes in water content near e
  Fine textured or poorly-aggregated soils
    Larger e
    Gradual changes in water content near e

## Slide 5
The measured and estimated soil water retention curves of Troup loamy sand (code no. 1012) (a) with fitted α and (b) with theoretical α. The fitted α value is higher than the theoretical one. TIS, totally impenetrable spheres model; FPS, fully penetrable spheres model; and VG, van Genuchten model
Chan, T.P., and R.S. Govindaraju. 2004. Estimating soil water retention curve from particle-size distribution data based on polydisperse sphere systems. Vadose Zone J. 3:1443-1454.

## Slide 6: Reading assignment
Soil water retention
  p. 116-123
  Hysteresis and Measurement of Soil-Moisture Potential

## Slide 7: Hysteresis
  Desorption curve: an initially wet soil is dried by applying increasing amounts of suction.
  Sorption curve: an initially dry soil is gradually wetted by reducing the suction.
  Hysteresis is the phenomenon when the desorption and sorption curves differ.
  From the Greek husterēsis, a shortcoming,
    from husterein, to be late
   for a given matric suction during sorption “comes short” of  during desorption

## Slide 9: Causes of hysteresis
  Nonuniform shape of individual pores: “ink bottle” effect

## Slide 10: Causes of hysteresis
  Contact angle hysteresis: contact angle is greater during wetting

## Slide 11: Causes of hysteresis
  Entrapped air
  Changes in soil structure: shrink-swell, etc…

## Slide 12: Factors influencing soil water retention
  Soil structure (b, aggregate size distribution)
    important at low suctions, 0 to 50 kPa
    *Note: 1 kPa = 10.2 cm H2O at 4C
    Capillary effects

## Slide 13
Insert 6.9
Comparison of measured and fitted water retention curves for homogenized soil samples from the Stagnic Chernozem Ah horizon (Hildesheim site) involving five different reference void ratios between 0.98 and 1.63 at saturation.
Stange, C.F., and R. Horn. 2005. Modeling the soil water retention curve for conditions of variable porosity. Vadose Zone J. 4:602-613.

## Slide 14: Factors influencing soil water retention
  Soil structure (b, aggregate size distribution)
    important at low suctions, 0 to 50 kPa
    Capillary effects
  Clay content
    Positively related to surface area of soil particles
    Positively related to water adsorption
    Dominant factors at high suctions

## Slide 15
Insert 6.8

## Slide 16: Factors influencing soil water retention
  Soil structure (b, aggregate size distribution)
    important at low suctions, 0 to 50 kPa
    Capillary effects
  Clay content
    Positively related to surface area of soil particles
    Positively related to water adsorption
    Dominant factors at high suctions
  Soil organic matter
    Reduces b
    Increases water retention at low suctions

## Slide 17: Models of soil water retention
  Brooks and Corey (1966)
  r = residual volumetric water content (at high suction)
  s = saturated volumetric water content
  e = air entry suction
   = pore size distribution index

## Slide 18: Models of soil water retention
  Van Genuchten (1980) (cited >3000 times)
   = fitting parameter inversely related to e
  n = fitting parameter which affects the shape of the curve
  m = fitting parameter often fixed as m = 1 – 1/n

## Slide 19: Measuring soil water retention curves
Hanging water column
Tempe cells
Pressure plates
http://web.ku.edu/~soil/Facilities_files/IMG_0141.jpg
http://www.ictinternational.com.au/images/extractor1400-2.gif

## Slide 20: Monitoring soil matric potential: tensiometer

## Slide 21: Monitoring soil matric potential: heat dissipation sensor
Campbell Scientific, Inc. 229 Heat dissipation sensor

## Slide 22: Estimating soil water content using the Mesonet’s CSI 229 sensors
Step 1: convert sensor reading to matric potential

## Slide 23: Estimating soil water content using the Mesonet’s CSI 229 sensors
  Step 2: convert matric potential to soil volumetric water content using van Genuchten’s equation
   = fitting parameter inversely related to e
  n = fitting parameter which affects the shape of the curve
  m = fitting parameter often fixed as m = 1 – 1/n

## Slide 24: Reading assignment
  Laminar Flow and Darcy’s Law, p. 127-136
  Homework 3 due Wednesday, Oct. 10